## Slide 1: Data-Level Parallelism Exploitation
Kai Bu
kaibu@zju.edu.cn
http://list.zju.edu.cn/kaibu/comparch2022
10

## Slide 2: Data-Level Parallelism

## Slide 3: Data-Level Parallelism
Loop
Notes: Examples focus on loop related code sequences

## Slide 4: Data-Level Parallelism
Loop
for (i=0, i<100, i=i+1)
X[i] = Y[i] + Z[i];
no dependence at all;
loop iterations can be fully parallelized;
Notes: No dependence, loop iterations can be fully run in parallel

## Slide 5: Data-Level Parallelism
Loop
for (i=0, i<100, i=i+1)
X[i] = a * Y[i] + X[i];
in-iteration dependence of X[i];
can be eliminated through loop unrolling or
vectorization;
Notes: Two uses of X[i] are dependent, but this dependence is within a single iteration:
Dependence can be eliminated through loop unrolling or vectorization;

## Slide 6: Data-Carried Dependence
Loop
for (i=0, i<100, i=i+1)
A[i+1] = A[i] + C[i]; /* S1 */
B[i+1] = B[i] + A[i+1]; /* S2 */
in-iteration dependence of A[i+1];
cross-iteration dependences: A[i], B[i] with
that produced in the earlier iteration
Notes: There are two different dependences:
S1 uses a value computed by S1 in an earlier iteration, because iteration i com- putes A[i + 1], which is read in iteration i + 1. The same is true of S2 for B[i] and B[i + 1].
S2 uses the value A[i+1] computed by S1 in the same iteration.

## Slide 7: Data-Carried Dependence
Loop
Data accesses in later iterations are dependent on data values produced in earlier iterations  Recurrence
Loop-carried dependence may not necessarily prevent parallelism
Notes: The analysis of loop-level parallelism focuses on determining whether data accesses in later iterations are dependent on data values produced in earlier itera- tions; such dependence is called a loop-carried dependence.
It is also possible to have a loop-carried dependence that does not prevent parallelism, as the next example shows.

## Slide 8: Data-Carried Dependence
Loop
Example loop

## Slide 9: Data-Carried Dependence
Loop
Example loop
In-iteration dependence: S1  S1: A[i]
Loop-carried dependence: S1  S2: B[i]
Notes: S1 relies on the value generated by S2 of the previous iteration.

## Slide 10: Data-Carried Dependence
Loop
Example loop
In-iteration dependence: S1  S1: A[i]
Loop-carried dependence: S1  S2: B[i]
No circular loop-carried dependence: self dependence, mutual dependence;
Notes: Cross-iteration self dependence, e.g.:
A[i+1] = A[i] + C[i];

## Slide 11: Data-Carried Dependence
Loop
Example loop
In-iteration dependence: S1  S1: A[i]
Loop-carried dependence: S1  S2: B[i]
No circular loop-carried dependence: can be Rewritten to run in parallel
Rewritten

## Slide 12: Data-Carried Dependence
Rewritten
Loop
Rewritten loop
Notes: The dependence between the two statements is no longer loop-carried so that iterations of the loop may be overlapped, provided the statements in each iteration are kept in order.

## Slide 13: how to find dependences?

## Slide 14: Index Affinity
One-dimensional array index is affine if it can be written in the form a x i + b, where a and b are constants and i is the loop index variable
Index of a multidimensional array is affine if the index in each dimension is affine

## Slide 15: Dependence Conditions
Two iteration indices, j and k, both within loop bounds: m <= j, k <= n;
Store into an array element indexed by a x j + b;
Fetch from that same array element indexed by c x k + d, that is: a x j + b = c x k + d
Notes: Determining whether there is a dependence between two references to the same array in a loop is thus equivalent to determining whether two affine functions can have the identical value for different indices between the bounds of the loop. For example, suppose we have stored to an array element with index value a ! i + b and loaded from the same array with index value c ! i + d, where i is the for-loop index variable that runs from m to n. A dependence exists if two conditions hold:
1. Therearetwoiterationindices,jandk,thatarebothwithinthelimitsofthefor- loop.Thatis,m j n,m k n.
2. Theloopstoresintoanarrayelementindexedbya!j+bandlaterfetchesfrom thatsamearrayelementwhenitisindexedbyc!k+d,thatis,a!j+b1⁄4c!k+d.

## Slide 16: GCD Test
a, b, c, and d are all constants
GCD (Greatest Common Divisor) Test: if a loop-carried dependence exists, (d - b)%GCD(c, a) = 0
no GCD  no loop-carried dependence
GCD ! loop-carried dependence because GCD test does not consider loop bounds

## Slide 17: GCD Test
a, b, c, and d are all constants
GCD (Greatest Common Divisor) Test: if a loop-carried dependence exists, (d - b)%GCD(c, a) = 0
Example:
a=2, b=3, c=2, d=0
(d-b)%GCD(2,2) = -3%2 !=0  no dep

## Slide 18: how to type dependences?

## Slide 19: Dependency Types
Example code

## Slide 20: Dependency Types
Example code
true dependence: Y[i]

## Slide 21: Dependency Types
Example code
antidependence: X[i]

## Slide 22: Dependency Types
Example code
antidependence: Y[i]

## Slide 23: Dependency Types
Example code
output dependence: Y[i]

## Slide 24: Dependency Types
Example code
remember register renaming?

## Slide 25: Dependency Types
remember register renaming?
Example code
false dependences eliminated
Elimination

## Slide 26: Dependency Types
remember register renaming?
Further example
Elimination
loop-carried dependence:
sum

## Slide 27: Dependency Types
remember register renaming?
Further example
Elimination
loop-carried dependence:
sum
scalar expansion:
sum  sum[i]

## Slide 28: Dependency Types
remember register renaming?
Further example
Elimination
loop-carried dependence:
sum
scalar expansion:
sum  sum[i]
vector sum:
in-loop scalar dep;

## Slide 29: Dependency Types
remember register renaming?
Further example
Elimination
loop-carried dependence:
sum
scalar expansion:
sum  sum[i]
vector sum:
in-loop scalar dep;
parallel reduction:
10 processors with further scalar expansion;
finalsum  finalsum[p]

## Slide 30: Dependency Types
remember register renaming?
Further example
Elimination
loop-carried dependence:
sum
scalar expansion:
sum  sum[i]
vector sum:
in-loop scalar dep;
parallel reduction:
10 processors with further scalar expansion;
finalsum  finalsum[p]
scalar loop to sum 10 finalsum[p];

## Slide 31: examples
Embedded GPU vs Server GPU
Embedded
Server

## Slide 32
Embedded
Server

## Slide 33: examples
CPU vs GPU
CPU
GPU

## Slide 34
CPU vs GPU
CPU
GPU
CPU
GPU
Notes: Figure4.27 IntelCorei7-960andNVIDIAGTX280.TherightmostcolumnshowstheratiosofGTX280toCorei7.For single-precision SIMD FLOPS on the GTX 280, the higher speed (933) comes from a very rare case of dual issuing of fused multiply-add and multiply. More reasonable is 622 for single fused multiply-adds. Note that these memory bandwidths are higher than in Figure 4.28 because these are DRAM pin bandwidths and those in Figure 4.28 are at the processors as measured by a benchmark program. From Table 2 in Lee, W.V., et al., 2010. Debunking the 100! GPU vs. CPU myth: an evaluation of throughput computing on CPU and GPU. In: Proc. 37th Annual Int’l. Sym- posium on Computer Architecture (ISCA), June 19–23, 2010, Saint-Malo, France.

## Slide 35
CPU
GPU
CPU vs GPU
CPU
GPU
Notes: Figure4.27 Intel Core i7-960 and NVIDIA GTX 280. The right most column shows the ratios of GTX 280 to Corei7. For single-precision SIMD FLOPS on the GTX 280, the higher speed (933) comes from a very rare case of dual issuing of fused multiply-add and multiply. More reasonable is 622 for single fused multiply-adds. Note that these memory bandwidths are higher than in Figure 4.28 because these are DRAM pin bandwidths and those in Figure 4.28 are at the processors as measured by a benchmark program. From Table 2 in Lee, W.V., et al., 2010. Debunking the 100! GPU vs. CPU myth: an evaluation of throughput computing on CPU and GPU. In: Proc. 37th Annual Int’l. Sym- posium on Computer Architecture (ISCA), June 19–23, 2010, Saint-Malo, France.

## Slide 36
Benchmarks
Notes: Figure 4.29 Throughput computing kernel characteristics. The name in parentheses identifies the benchmark name in this section. The authors suggest that code for both machines had equal optimization effort. From Table 1 in Lee, W.V., et al., 2010. Debunking the 100! GPU vs. CPU myth: an evaluation of throughput computing on CPU and GPU. In: Proc. 37th Annual Int’l. Symposium on Computer Architecture (ISCA), June 19–23, 2010, Saint- Malo, France.
The researchers said that they selected the benchmark programs by analyzing the computational and memory characteristics of four recently proposed bench- mark suites and then “formulated the set of throughput computing kernels that cap- ture these characteristics.” Figure 4.29 describes these 14 kernels, and Figure 4.30 shows the performance results, with larger numbers meaning faster.

## Slide 37: Performance
Notes: Figure 4.30 Raw and relative performance measured for the two platforms. In this study, SAXPY is used only as a measure of memory bandwidth, so the right unit is GB/s and not GFLOP/s. Based on Table 3 in Lee, W.V., et al., 2010. Debunking the 100! GPU vs. CPU myth: an evaluation of throughput computing on CPU and GPU. In: Proc. 37th Annual Int’l. Symposium on Computer Architecture (ISCA), June 19–23, 2010, Saint-Malo, France.

## Slide 38: examples
CPU vs GPU: updated
CPU
GPU

## Slide 39
CPU vs GPU
CPU
GPU
Notes: Figure 4.31 Intel Xeon Platinum 8180 and NVIDIA P100. The rightmost column shows the ratios of P100 to the Xeon. Note that these memory bandwidths are higher than in Figure 4.28 because these are DRAM pin bandwidths and those in Figure 4.28 are at the processors as measured by a benchmark program.

## Slide 40
CPU
GPU
Notes: Figure 4.33 Roofline models of older and newer CPUs versus older and newer GPUs. The higher roofline for each computer is single-precision floating-point performance, and the lower one is double-precision performance.

## Slide 41: Performance
GPU is 2~5 times faster than CPU
Notes: Figure4.32 Raw and relative performance measured for modern versions of the two platforms as compared to the relative performance of the original platforms. Like Figure 4.30, SAXPY and DAXPY are used only as a measure of memory bandwidth, so the proper unit is GB/s and not GFLOP/s.

## Slide 42: Review
Loop-carried dependence
Dependency types
Dependency elimination

## Slide 43
Chapter 4.5-4.9
Notes: The following content corresponds to chapter 3 (mostly 3.3 – 3.14)
atop the basic working principles of pipelining we have learnt from Appendix C.

## Slide 44: ?

## Slide 45
Thank You
to resonate
promise me a space
in your house of memories

## Slide 46: #What’s More
Life’s Big Adventure by Audiomachine
The Best Things in Life by Audiomachine